## Slide 1
NEYER GAP TEST V1.14
Neyer Gap Test
Finding the transition between Interaction and No interaction
smaller gap
larger gap
Interaction more likely
transition area
No interaction more likely
Each completed test helps the tool choose the next useful gap.
The final study estimates the middle gap, overall variation and probability curve.
Neyer Gap Test V1.14
Notes: Conceptual introduction to the V1.14 direct gap study. Orange and blue dots represent the two possible physical outcomes. The mixed results near the centre illustrate the transition area that the adaptive test is designed to study.

## Slide 2
02
How the tool turns tests into a curve
INPUT
What the user provides
Low and high middle-gap guesses
Permitted gap range
Usable gap step
Maximum number of tests
ADAPTIVE TEST LOOP
1 Tool requests a reachable gap
2 User builds and measures once
3 User records the physical outcome
4 Tool selects the next useful gap
repeat until the planned test limit
OUTPUT
What the study produces
Estimated middle gap
Overall variation
Probability curve
Complete test record
The measured gap stays attached to the outcome that physically occurred.
Neyer Gap Test V1.14
Notes: This workflow describes the V1.14 direct gap study. It deliberately excludes the separate pre-lab and fixed-gap qualification topics.

## Slide 3
03
What the gap study is finding
Chart: Estimated chance of interaction
| 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1 | 1.2 | 1.4 | 1.6 | 1.8 | 2 | 2.2 | 2.4 | 2.6 | 2.8 | 3 | 3.2 | 3.4 | 3.6 | 3.8 | 4 | 4.2 | 4.4 | 4.6 | 4.8 | 5 | 5.2 | 5.4 | 5.6 | 5.8 | 6 | 6.2 | 6.4 | 6.6 | 6.8 | 7 | 7.2 | 7.4 | 7.6 | 7.8 | 8 | 8.2 | 8.4 | 8.6 | 8.8 | 9 | 9.2 | 9.4 | 9.6 | 9.8 | 10
Fitted chance of interaction | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 99.99 | 99.99 | 99.97 | 99.94 | 99.89 | 99.8 | 99.63 | 99.36 | 98.92 | 98.24 | 97.21 | 95.74 | 93.69 | 90.94 | 87.39 | 82.97 | 77.66 | 71.52 | 64.68 | 57.32 | 49.7 | 42.09 | 34.77 | 27.97 | 21.89 | 16.65 | 12.3 | 8.82 | 6.13 | 4.13 | 2.69 | 1.7 | 1.04 | 0.61 | 0.35 | 0.19 | 0.1 | 0.05 | 0.03 | 0.01 | 0.01 | 0 | 0 | 0
Interaction test | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
No interaction test | 0 | 0 | 0 | 0 | 0 | 0 | 0
Verified reference replay
20
entered test outcomes
5.3922 mm
estimated middle gap
1.0412 mm
estimated overall variation
Smaller gaps produced more Interaction results in this verified reference example.
Neyer Gap Test V1.14
Notes: Source: audit/v114/paper-reference.txt and audit/v114/validation-summary.txt. The dots show all 20 outcomes from the verified published-example replay. The curve uses the verified middle gap 5.3922 mm and overall variation 1.0412 mm.

## Slide 4
04
How the next useful gap is selected
smaller gap
larger gap
Interaction
No interaction
next request
STAGE 1
Find both outcomes
STAGE 2, PART 1
Halve the wide separation
STAGE 2, PART 2
Probe closer; width × 0.8
D-OPTIMAL
Add the most information
nearest reachable setting
Conceptual view. The requested value is moved to the nearest reachable physical setting.
Neyer Gap Test V1.14
Notes: Conceptual view of the verified V1.14 selection sequence. Stage 1 finds both outcomes. Stage 2 Part 1 halves a wide separation. Stage 2 Part 2 uses repeated probes with the working variation multiplied by 0.8. After outcome overlap exists, D-optimal selection chooses an information-rich next target, then the physical model maps it to a reachable setting.